## Slide 1: Physical Unclonable Functions

## Slide 2: What are Physical Unclonable Functions?
A PUF is a physical object or process.
It can be used as a unique identifier, or can be used as part of a cryptographic process
They make use of the natural randomness of some physical medium in order to be unique.

## Slide 3: Some Examples of PUFs
The most natural example is that of our fignerprints
SRAM can be used as a PUF due to each cell’s unique startup pattern
Credit Cards contain a Ferrous Oxide coating that, combined with the written data, create a PUF
An optical variant of PUFs can be seen by shining a laser through light scattering particles, and observing the speckle pattern

## Slide 4: My Proposed PUF
When somebody writes their signature, there will always be some variation between signings
If they were to scratch their signature into a conductive film, a current could then be passed through the film, and the film would have a unpredictable resistance.
The resistance, when paired with part of the document being signed, could be hashed and give a unique identity.

## Slide 5: The Experiment
Cut rectangles of graphene, and scratch a ‘signature’ onto them.
Run a current through the rectangles and note the resistance.
In six samples ‘signatures’, there was a notable variation between the resistance of each signature.
Thus, the different ‘signatures’ did give a different resistance and could theoretically be used.

## Slide 6: Future Work
While this was successful, the resistance given and the range of values is too low to be used on a larger scale.
This could be addressed by different materials or having different measurement points.
Another option could be to use something similar to the Ferrous Oxide coating in credit cards, and look at the magnetic profile.